## Slide 1: Our new Zero Energy home
Diane & John Burke

## Slide 2: Agenda
5 Principles of Passive House
How is it working so far?
Living in it
Organic Garden& Native Plants
Q&A

## Slide 3: 5 Principles of Passive House
No Thermal Bridging
Walls, floors, and roofs are well insulated with no gaps. This reduces heating and cooling requirements.
Superior Windows
Windows are the biggest source of heat transfer. Triple Pane windows are more than twice as efficient as double pane.
Energy Recovery Ventilation
An ERV recovers heat from stale used air and transfers it to fresh incoming air. Heat Pumps are used for heating and cooling.
Quality Construction
Quality construction is key to successful accomplishment of objectives. Insulation serves to minimize heat transfer.
Air-Tight Construction
There should be no uncontrolled airflow between the external and internal environment.

## Slide 4: No Thermal Bridging
Walls 18” thick, Packed cellulose insulation
Foundation 5’ deep and insulated

## Slide 5: Superior Windows
Triple Pane Windows
Double Pane = 3.4 R value
Triple Pane = 7.5 R value

## Slide 6: Energy Recovery Ventilation (ERV)
ERV unit
Zehnder ComfoAir
ERV Efficiency
Zehnder App
ERV recovers about 90% of heat/cool temp
Also controls humidity

## Slide 7: Heat Pumps
How Heat Pumps work
Heat Pumps are Electro-mechanical
No burning of carbon-based fuels
Not electric resistance (baseboard) heaters
Heats in winter, cools in summer
Based upon latent heat of evaporation and condensation

## Slide 8: Quality Construction
Panels built in factory Minimal waste
Carefully assembled on site

## Slide 9: Air-Tight Construction
Blower Door Test

## Slide 10: How’s it working so far?
 | Passive Standard | Our House | 
Primary Energy Use | <= 60 kWh/M2/yr | 54.4 kWh/M2/yr | 
Airtightness | <= 0.60 ACH50 | 0.227 ACH50 | 
Thermal Comfort | <= 10% > 25C (77F) | TBD, but I wouldn’t bet against it | 

## Slide 11: Estimated Energy Usage

## Slide 12: Problems and obstacles
Inflation! - Building materials are up a lot more than PCE,CPI
Variances and permits –Normal stuff...
Finding a Passive savvy General Contractor - Key
Can’t permeate thermal barrier
No basement
300 ft to power & new telephone pole and transformer

## Slide 13: Living in it
We love it!
Feels more solid and quiet than a regular house
Always comfortable. No more thermostat battles
Air quality is great. No dust or humidity

## Slide 14: Organic Garden
Organically grown vegetables, fruits, spices, and flowers
No pesticides or fertilizers

## Slide 15: Organic Honey
5 bee colonies
11 acres devoted to supporting Bees
We seed clover annually

## Slide 16: Native Plants
Native plants are important because they provide food and housing for local wildlife
We have Oak, Holly, Beech, Birch, Elm, sunflowers, Milkweed, Echinacea

## Slide 17: Thank you
Diane & John Burke| dburke.yoga@gmail.com